Tray Definition Modification Protocol

The files are located in

C:/Program Files/Formulatrix/Formulator/DataFiles

Within the software Formulator, with the instrument on:

First to see the names of the config files go to

File, New, Dispense List

Then to modify a config file

File, Open, Microplate Definition

Example: VDXm 24 Well (called PT4-24-Hampton) the height is 11 mm z=14.4 and -2 on each line. Right click in the line # - move to position

Note: PT5-48 needs modifications, drips off the sides of the wells.

In the software Rockmaker, in the folder tree on the left:

Setup, Containers

Once inside use right click to add a container